## Slide 1: EDES 301 Inclusive, Low-Resource Pulse Oximeter Proposal
10/04/2026
Cristian Castillo

## Slide 2: Background Information
  Blood oxygen level is a physiological stat that reports how much oxygen your red blood vessels are carrying from your lungs to every other tissue in your body.
  Low oxygen levels can be signs of hypoxia and report a greater issue in your body. Thus, a dropping blood oxygen level is a great sign for the need to receive treatment prior to organ failure
  Currently, there exists no pulse oximeter that is commercially available that eliminates racial bias. There exists a need to develop a low-cost oximeter that can be used across skin pigmentations.

## Slide 3: System Block Diagram
Power (3.3 V) (PocketBeagle)
LED’s
Red + IR
Photodiode
18-bit ADC
MAX30102 module
Finger
TCS34725
RGB color sensor
White LED, skin tone
PocketBeagle (software pipeline)
Signal Filtering
(AC/DC Extraction)
Reference Data
(Ground-Truth Pairs)
Ratio of ratios
(R from red and IR)
Calibration model
(corrected Sp02)
Tone classifier
(RGB to tone score)
Display
Sp02, pulse rate
Data log
SD card

## Slide 4: Power Block Diagram
Power (3.3 V) (PocketBeagle)
IR LED
Red LED
Finger
IR Photodiode
Photodiode
Signal Conditioning
Display
Skin tone sensor (TCS34725)

## Slide 5: Components / Budget
Component | EDES301 to Buy? | Cost
2Pcs Heart Rate Sensor Module MAX30102 Blood Oxygen Sensor Pulse Detections (https://www.amazon.com/dp/B094JC48HQ?lv=shuf&channelId=500&plpRedirect=mhFallback) | Yes | 7.99
RGB Color sensor with IR filter and White LED – TCS34725 (https://www.adafruit.com/product/1334?srsltid=AU7gw4WtW3GIkzt8NsHEu7ddisuv012--SP7927BKlD0fxF_SfNch-74) | Yes ? | 7.95
3D printed casing for finger sensor | No | Print dependent
Wires, resistors, etc. | No | OEDK